## Slide 1: CMOS VLSI Design Lecture 8: Power
Notes: Hello and welcome to the CMOS VLSI Design course.

## Slide 2: Learning Objectives
At the end of this lecture, you should be able to:
Use equations to explain the sources of power dissipation in a chip.
Estimate dynamic and static power consumption.
Describe methods to reduce dynamic and static power losses.
Notes: By the end of this course, you should be able to:
Use equations to explain the sources of power dissipation in a chip.
Estimate dynamic and static power consumption.
Describe methods to reduce dynamic and static power losses.

## Slide 3: Power and Energy
Power is drawn from a voltage source attached to the VDD pin(s) of a chip.
Instantaneous Power:
Energy:
Average Power:
Notes: The power is drawn from a voltage source attached to vdd pin(s) of a chip.
The amount of power in a circuit at a given instant in time is called the instantaneous power and can be calculated by the current times voltage in T time
Energy is the ability to do work or apply force to move an object. In electrical circuits, energy is measured as power over time or as integral of instantaneous power.
The average power is the amount of work done or energy converted per unit time; it can be calculated by dividing the energy over time.

## Slide 4: Power in Circuit Elements
Notes: Power in circuit elements:
Instantaneous power is Idd(t) X Vdd. Where Idd is the current through the element and Vdd is the voltage across the element.
The power consumed by a resistor. This power is converted to heat and is given by Ir X Ir X R. Where Ir is the current through the resistor.
The charge stored in a capacitor which is given by the formula for Ec.
  We can calculate the energy stored in a capacitor by taking the integral of the current times V in t times for the interval zero to infinity, which is the same as the integral of the capacitance times change of voltage over time by the same limits that implies. Ec is equal to C times integral V from the limits 0 to Vc or ½ of the capacitance times square voltage capacitance.

## Slide 5: Charging a Capacitor
When the gate output rises
  Energy stored in the capacitor is
  But energy drawn from the supply is
  Half the energy from VDD is dissipated in the pMOS transistor as heat and other half stored in capacitor
When the gate output falls
  Energy in the capacitor is dumped to GND
  Dissipated as heat in the nMOS transistor
Notes: Look at this load capacitance in the CMOS circuit, when the gate output rises the capacitor charges, and this energy can be calculated by Ec equals to ½ of CL times square VDD.
Half the energy from Vdd will be dissipated in the pMOS transistor as heat and other half stored in the capacitor
When the gate output falls, the energy in the capacitor is dumped to GND and dissipated as heat in the nMOS transistor.

## Slide 6: Switching Waveforms
Example: VDD = 1.0 V, CL = 150 fF, f = 1 GHz
Notes: Let’s assume that cmos inverter has a vdd of 1 volt, a load capacitance of 150 femtofarads, its switching frequency is 1 GHz.
With this, we can plot different switching waveforms and compare the power related to nmos, pmos, and loading capacitance.

## Slide 7: Switching Power
Notes: Slide derives the power consumed by a switching inverter.
The main factors are the load capacitance C, the operating voltage Vdd and the switching frequency.

## Slide 8: Activity Factor
Suppose the system clock frequency = f
Let fsw = a f, where a = activity factor
  If the signal is a clock, a = 1
  If the signal switches once per cycle, a = ½
Dynamic power:
Notes: Activity factor is the fraction of the system clock frequency in which the gate changes output.

## Slide 9: Short Circuit Current
When transistors switch, both nMOS and pMOS networks may be momentarily ON at once
Leads to a blip of “short circuit” current.
<10% of dynamic power if rise/fall times are comparable for input and output
We will generally ignore this component
Notes: When transistors switch, both nMOS and pMOS networks may be momentarily ON at once; this can lead to a blip of “short circuit” current. This value is less than 10% of dynamic power if the rise/fall times are comparable for input and output, so we will generally ignore this component.

## Slide 10: Power Dissipation Sources
Ptotal = Pdynamic + Pstatic
Dynamic power: Pdynamic = Pswitching + Pshort circuit
  Switching load capacitances
  Short-circuit current
Static power: Pstatic = (Isub + Igate + Ijunct + Icontention)VDD
  Subthreshold leakage
  Gate leakage
  Junction leakage
  Contention current
Notes: Total power dissipated in a circuit is the sum of dynamic and static power.
Dynamic power is equal to switching power plus the short circuit power.
Static power is equal to the product of the operating voltage and the total of subthreshold, gate leakage, junction leakage, contention currents.

## Slide 11: Dynamic Power Example
1 billion transistor chip
  50 M logic transistors
    Average width: 12 λ
    Activity factor = 0.1
  950 M memory transistors
    Average width: 4 λ
    Activity factor = 0.02
  1.0 V 65 nm process
  C = 1 fF/μm (gate) + 0.8 fF/μm (diffusion)
Estimate dynamic power consumption @ 1 GHz. Neglect wire capacitance and short-circuit current.

## Slide 12: Solution
Notes: Calculate the total logic and memory capacitance of the system. Calculate the switching power for the logic and memory and add them to obtain the total dynamic power.

## Slide 13: Dynamic Power Reduction
Try to minimize:
  Activity factor
  Capacitance
  Supply voltage
  Frequency
Notes: In order to reduce the switching power, you can try to minimize:
the activity factor
capacitance
supply voltage and
frequency

## Slide 14: Activity Factor Estimation
Let Pi = Prob(node i = 1)
  Pi = 1-Pi
ai = Pi * Pi
Completely random data have P = 0.5 and a = 0.25
Data are often not completely random
  e.g., upper bits of 64-bit words representing bank account balances are usually 0
Data propagating through ANDs and ORs have lower activity factor
  Depends on design, but typically a ≈ 0.1

## Slide 15: Switching Probability
Notes: Switching probability calculation for different gates.

## Slide 16: Example
A 4-input AND is built out of two levels of gates
Estimate the activity factor at each node if the inputs have P = 0.5
Notes: Example, a 4-input AND is built out of two levels of gates. Estimate the activity factor at each node if the inputs have a probability of 0.5 when switching.
So let’s look at the first two nodes (NAND2); the same process is applied to both.
The probability of getting 1 as an output is ¾ and 0 is ¼ (1 - ¾)
The switching probability for NAND2 = ¾ X ¼ = 3/16.
For the NOR2, switching probability = multiplication of the not probability of two NAND2 (¼ X ¼ ). The not switching probability of the NOR2 = 1 – 1/16 = 15/16
Therefore, the switching probability = 1/16 X 15/16 = 15/256.

## Slide 17: Clock Gating
The best way to reduce the activity is to turn off the clock to registers in unused blocks
  Saves clock activity (a = 1)
  Eliminates all switching activity in the block
  Requires determining if block will be used
Notes: Clock gating is used to turn off the clock to registers in unused block. This method is applied to reduce dynamic power consumption.

## Slide 18: Capacitance
Gate capacitance
  Fewer stages of logic
  Small gate sizes
Wire capacitance
  Good floor planning to keep communicating blocks close to each other
  Drive long wires with inverters or buffers rather than complex gates
Notes: Reduced stages of logic and gate sizing (small gate size) can be used to save dynamic power consumption.
Wires have capacitance too. Proper floor planning of the layout can ensure that communicating blocks are close to each other and long wires are driven with inverters.

## Slide 19: Voltage/Frequency
Run each block at the lowest possible voltage and frequency that meets performance requirements
Voltage Domains
  Provide separate supplies to different blocks
  Level converters required when crossing
  from low to high VDD domains
Dynamic Voltage Scaling
  Adjust VDD and f according to
  workload
Notes: To minimize dynamic power consumption, the voltage and frequency of operation can be scaled.

## Slide 20: Static Power
Static power is consumed even when chip is quiescent.
  Leakage draws power from nominally OFF devices
  Ratioed circuits burn power in fight between ON transistors
Notes: Static power is consumed even when chips are inactive.

## Slide 21: Static Power Example
Revisit power estimation for 1 billion transistor chip
Estimate static power consumption
  Subthreshold leakage
    Normal Vt: 100 nA/mm
    High Vt: 10 nA/mm
    High Vt used in all memories and in 95% of logic gates
  Gate leakage 5 nA/mm
  Junction leakage negligible

## Slide 22: Solution

## Slide 23: Subthreshold Leakage
For Vds > 50 mV
Ioff = leakage at Vgs = 0, Vds = VDD
Typical values in 65 nm
Ioff = 100 nA/mm @ Vt = 0.3 V
Ioff = 10 nA/mm @ Vt = 0.4 V
Ioff = 1 nA/mm @ Vt = 0.5 V
h = 0.1
kg = 0.1
S = 100 mV/decade

## Slide 24: Stack Effect
Series OFF transistors have less leakage
  Vx > 0, so N2 has negative Vgs
  Leakage through 2-stack reduces ~10x
  Leakage through 3-stack reduces further
Notes: The stack effect is when series OFF transistors have less leakage, so x voltage > 0, so nmos transistor 2 has negative ground source voltage.

## Slide 25: Leakage Control
Leakage and delay trade off
  Aim for low leakage in sleep and low delay in active mode
To reduce leakage:
  Increase Vt: multiple Vt
    Use low Vt only in critical circuits
  Increase Vs: stack effect
    Input vector control in sleep
  Decrease Vb
    Reverse body bias in sleep
    Or forward body bias in active mode
Notes: There is a leakage and delay trade off; we aim for low leakage in sleep and low delay in active mode.
To reduce leakage:
Increase the threshold voltage and use low threshold voltage only in critical circuits.
Increase the source voltage so you can have a stack effect.
Decrease the body voltage by reversing body bias in sleep or forward body bias in active mode.

## Slide 26: Gate Leakage
Extremely strong function of tox and Vgs
  Negligible for older processes
  Approaches subthreshold leakage at 65 nm and below in some processes
An order of magnitude less for pMOS than nMOS
Control leakage in the process using tox > 10.5 Å
  High-k gate dielectrics help
  Some processes provide multiple tox
    e.g., thicker oxide for 3.3 V I/O transistors
Control leakage in circuits by limiting VDD

## Slide 27: NAND3 Leakage Example
100 nm process
  Ign = 6.3 nA Igp = 0
  Ioffn = 5.63 nA Ioffp = 9.3 nA
Data from [Lee03]

## Slide 28: Junction Leakage
From reverse-biased p-n junctions
  Between diffusion and substrate or well
Ordinary diode leakage is negligible
Band-to-band tunneling (BTBT) can be significant
  Especially in high-Vt transistors where other leakage is small
  Worst at Vdb = VDD
Gate-induced drain leakage (GIDL) exacerbates
  Worst for Vgd = -VDD (or more negative)
Notes: Junction leakage occurs into the substrate/well from the reverse-biased p-n junction between diffusion and substrate/well.

## Slide 29: Power Gating
Turn OFF power to blocks when they are idle to save leakage
  Use virtual VDD (VDDV)
  Gate outputs to prevent
  invalid logic levels to next block
Voltage drop across sleep transistor degrades performance during normal operation
  Size the transistor wide enough to minimize impact
Switching wide sleep transistor costs dynamic power
  Only justified when circuit sleeps long enough
Notes: To reduce leakage, turn off power to blocks when they are idle. Use virtual VDD, gate outputs to prevent invalid logic levels to next block.
Voltage drops occurs across sleep transistors. This degrades performance during normal operation, size the transistor wide enough to minimize this impact.
Reduce using switching wide sleep transistors due to its cost of dynamic power.