## Slide 1: CMOS VLSI Design Lecture 10: SPICE Simulation
Notes: Hello and welcome to CMOS VLSI design course; today our focus will be on SPICE Simulation.

## Slide 2: Learning Objectives
At the end of this lecture, you should be able to:
Simulate circuits with SPICE to determine DC transfer characteristics, Transient response and Power consumption.
Compare and confirm logical effort estimates through SPICE simulation.
Use SPICE to optimize circuit designs.
Notes: At the end of this lecture, you should be able to:
Use spice to predict the behavior of integrated circuits, confirm logical effort estimates through SPICE simulation, and use SPICE to optimize circuit designs.

## Slide 3: Introduction to SPICE
Simulation Program with Integrated Circuit Emphasis
  Developed in 1970’s at Berkeley
  Many commercial versions are available
  HSPICE is a robust industry standard
    Has many enhancements that we will use
Written in FORTRAN for punch-card machines
  Circuit elements are called cards
  Complete description is called a SPICE deck
Notes: Introducing the Simulation Program with Integrated circuit emphasis or SPICE. This program was developed in 1970’s at Berkeley, and there are many commercials versions available.
HSPICE is a robust industry standard that has many enhancements that we will use.

## Slide 4: Writing Spice Decks
Writing a SPICE deck is like writing a good program
  Plan: sketch schematic on paper or in editor
    Modify existing decks whenever possible
  Code: strive for clarity
    Start with name, email, date, purpose
    Generously comment
  Test:
    Predict what the results should be
    Compare with actual
    Garbage In, Garbage Out!
Notes: The process of writing a SPICE deck is like writing a good program.
You first need to plan, sketch schematic on paper or in editor.
Then, you will need to code your design striving for clarity and best practices.
Finally, test your design, predicting what results should be, compare the simulation with the actual circuit.

## Slide 5: Example: RC Circuit
* rc.sp
* David_Harris@hmc.edu 2/2/03
* Find the response of RC circuit to rising input
*------------------------------------------------
* Parameters and models
*------------------------------------------------
.option post
*------------------------------------------------
* Simulation netlist
*------------------------------------------------
Vin in gnd pwl 0ps 0 100ps 0 150ps 1.0 1ns 1.0
R1 in out 2k
C1 out gnd 100f
*------------------------------------------------
* Stimulus
*------------------------------------------------
.tran 20ps 1ns
.plot v(in) v(out)
.end
Notes: Look at this resistor-capacitor circuit written in SPICE.
Any line starting with a “*” is a comment and is ignored; Using comment, you can add the name of your spice file, your email, last date modified, and the purpose of the code.
Graphics results will be stored in binary file using .option post.
Simulate circuit using the simulation netlist.
Add stimulus, this example shows a stimulus for 1 nanosecond and a transition 20 ps.
Plot the voltage in and voltage out on the same graph.

## Slide 6: Result (Graphical)
Notes: The result that you will get is similar to this.

## Slide 7: Sources
DC Source
  Vdd vdd gnd 2.5
Piecewise Linear Source
  Vin in gnd pwl 0ps 0 100ps 0 150ps 1.0 1ns 1.0
Pulsed Source
  Vck clk gnd PULSE 0 1.0 0ps 100ps 300ps 800ps
Notes: We could add different types of sources in our simulation like:
DC source, piecewise linear source, and pulsed source.

## Slide 8: SPICE Elements
Letter
Element
R
Resistor
C
Capacitor
L
Inductor
K
Mutual Inductor
V
Independent voltage source
I
Independent current source
M
MOSFET
D
Diode
Q
Bipolar transistor
W
Lossy transmission line
X
Subcircuit
E
Voltage-controlled voltage source
G
Voltage-controlled current source
H
Current-controlled voltage source
F
Current-controlled current source
Notes: We could add different types of elements to our simulation using its letter as shown in the table.

## Slide 9: Units
Letter | Unit | Magnitude
a | atto | 10-18
f | fempto | 10-15
p | pico | 10-12
n | nano | 10-9
u | micro | 10-6
m | milli | 10-3
k | kilo | 103
x | mega | 106
g | giga | 109
E.g., 100 femptofarad capacitor = 100fF, 100f, 100e-15
Notes: As well as different type of units

## Slide 10: DC Analysis
* mosiv.sp
*------------------------------------------------
* Parameters and models
*------------------------------------------------
.include '../models/ibm065/models.sp'
.temp 70
.option post
*------------------------------------------------
* Simulation netlist
*------------------------------------------------
*nmos
Vgs g gnd 0
Vds d gnd 0
M1 d g gnd gnd NMOS W=100n L=50n
*------------------------------------------------
* Stimulus
*------------------------------------------------
.dc Vds 0 1.0 0.05 SWEEP Vgs 0 1.0 0.2
.end
Notes: DC analysis can be done using SPICE. In this case, we are simulating nmos transistor.

## Slide 11: I-V Characteristics
nMOS I-V
  Vgs dependence
  Saturation
Notes: That will give you this current-voltage characteristics.

## Slide 12: MOSFET Elements
M element for MOSFET
Mname drain gate source body type
+ W=<width> L=<length>
+ AS=<area source> AD = <area drain>
+ PS=<perimeter source> PD=<perimeter drain>
Notes: To place MOSFET elements in the simulation, you need to fill the following sequence.
M, then write a name, then specify the drain, gate, source, body, and type (NMOS or PMOS)
In addition to that, you could define the width and length of your transistor with the letter W and L as well as the area source, area drain, perimeter source, and perimeter drain.

## Slide 13: Transient Analysis
* inv.sp
* Parameters and models
*------------------------------------------------
.param SUPPLY=1.0
.option scale=25n
.include '../models/ibm065/models.sp'
.temp 70
.option post
* Simulation netlist
*------------------------------------------------
Vdd vdd gnd 'SUPPLY'
Vin a gnd PULSE 0 'SUPPLY’ 50ps 0ps 0ps 100ps 200ps
M1 y a gnd gnd NMOS W=4 L=2
+ AS=20 PS=18 AD=20 PD=18
M2 y a vdd vdd PMOS W=8 L=2
+ AS=40 PS=26 AD=40 PD=26
* Stimulus
*------------------------------------------------
.tran 0.1ps 80ps
.end
Notes: Transient analysis can also be done in SPICE.

## Slide 14: Transient Results
Unloaded inverter
  Overshoot
  Very fast
  edges
Notes: In the case of unloaded inverter, the transients result will look like this with overshot and very fast edges.

## Slide 15: Subcircuits
Declare common elements as subcircuits
E.g., fanout-of-4 Inverter Delay
  Reuse inv
  Shaping
  Loading
.subckt inv a y N=4 P=8
M1 y a gnd gnd NMOS W='N' L=2
+ AS='N*5' PS='2*N+10' AD='N*5' PD='2*N+10'
M2 y a vdd vdd PMOS W='P' L=2
+ AS='P*5' PS='2*P+10' AD='P*5' PD='2*P+10'
.ends
Notes: In SPICE, you can even declare common elements as subcircuits like the snippet show. That will create an unloaded inverter, then you can combine like a fanout-of-4 inverter delay.

## Slide 16: FO4 Inverter Delay
.end
* fo4.sp
* Parameters and models
*----------------------------------------------------------------------
.param SUPPLY=1.0
.param H=4
.option scale=25n
.include '../models/ibm065/models.sp'
.temp 70
.option post
* Subcircuits
*----------------------------------------------------------------------
.global vdd gnd
.include '../lib/inv.sp'
* Simulation netlist
*----------------------------------------------------------------------
Vdd vdd gnd 'SUPPLY'
Vin a gnd PULSE 0 'SUPPLY' 0ps 20ps 20ps 120ps 280ps
X1 a b inv * shape input waveform
X2 b c inv M='H' * reshape input waveform
Notes: Here is the snippet code to implement the fanout-of-4 inverter delay.
First, define a parameter of supply and H, scale, importing the models, add the temperature, and get bitstream of the program.
Then, import the circuit that we have defined and make global vdd and gnd.
After that, add the stimulation netlist.

## Slide 17: FO4 Inverter Delay Cont.
X3 c d inv M='H**2' * device under test
X4 d e inv M='H**3' * load
x5 e f inv M='H**4' * load on load
* Stimulus
*----------------------------------------------------------------------
.tran 0.1ps 280ps
.measure tpdr * rising prop delay
+ TRIG v(c) VAL='SUPPLY/2' FALL=1
+ TARG v(d) VAL='SUPPLY/2' RISE=1
.measure tpdf * falling prop delay
+ TRIG v(c) VAL='SUPPLY/2' RISE=1
+ TARG v(d) VAL='SUPPLY/2' FALL=1
.measure tpd param='(tpdr+tpdf)/2' * average prop delay
.measure trise * rise time
+ TRIG v(d) VAL='0.2*SUPPLY' RISE=1
+ TARG v(d) VAL='0.8*SUPPLY' RISE=1
.measure tfall * fall time
+ TRIG v(d) VAL='0.8*SUPPLY' FALL=1
+ TARG v(d) VAL='0.2*SUPPLY' FALL=1
.end
Notes: And finally, add the stimulus for this circuit; we can set triggers to capture important values with '.measure' and adding a trigger and a target, for example, the rising, falling, and average propagation delay along with the rise time and fall time.

## Slide 18: FO4 Results
Notes: Implementing this circuit will result in the following wave generated in SPICE.

## Slide 19: Optimization
HSPICE can automatically adjust parameters
  Seek value that optimizes some measurement
Example: Best P/N ratio
  We’ve assumed 2:1 gives equal rise/fall delays
  But we see the rise is actually slower than the fall
  What P/N ratio gives equal delays?
Strategies
  (1) run a bunch of sims with different P size
  (2) let HSPICE optimizer do it for us
Notes: HPSICE can automatically adjust parameter, for example, best P/N ratio or for each pmos transistor. How many nmos should we have?
So we have assumed 2:1 gives equal rise/fall delays, but you can see that the rise is actually slower than the fall.
To know which P/N ratio gives equal delays, we can use two different strategies:
1.- run a bunch of sims with different P size
2.- let HSPICE optimizer do it for us

## Slide 20: P/N Optimization
* fo4opt.sp
* Parameters and models
*----------------------------------------------------------------------
.param SUPPLY=1.0
.option scale=25n
.include '../models/ibm065/models.sp'
.temp 70
.option post
* Subcircuits
*----------------------------------------------------------------------
.global vdd gnd
.include '../lib/inv.sp'
* Simulation netlist
*----------------------------------------------------------------------
Vdd vdd gnd 'SUPPLY'
Vin a gnd PULSE 0 'SUPPLY' 0ps 20ps 20ps 120ps 280ps
X1 a b inv P='P1' * shape input waveform
X2 b c inv P='P1' M=4 * reshape input
X3 c d inv P='P1' M=16 * device under test
Notes: To add an optimization, we need to equal P from the simulation netlist to a parameter P1 that is defined in the next slide.

## Slide 21: P/N Optimization
X4 d e inv P='P1' M=64 * load
X5 e f inv P='P1' M=256 * load on load
* Optimization setup
*----------------------------------------------------------------------
.param P1=optrange(8,4,16) * search from 4 to 16, guess 8
.model optmod opt itropt=30 * maximum of 30 iterations
.measure bestratio param='P1/4' * compute best P/N ratio
* Stimulus
*----------------------------------------------------------------------
.tran 0.1ps 280ps SWEEP OPTIMIZE=optrange RESULTS=diff MODEL=optmod
.measure tpdr * rising propagation delay
+ TRIG v(c) VAL='SUPPLY/2' FALL=1
+ TARG v(d) VAL='SUPPLY/2' RISE=1
.measure tpdf * falling propagation delay
+ TRIG v(c) VAL='SUPPLY/2' RISE=1
+ TARG v(d) VAL='SUPPLY/2' FALL=1
.measure tpd param='(tpdr+tpdf)/2' goal=0 * average prop delay
.measure diff param='tpdr-tpdf' goal = 0 * diff between delays
.end
Notes: Then, here we will define P1 from 4 to 16 values.
The next command defines the number of iteration of the model.
Then, we use .measure to compute the best P/N ration.
Finally, add the stimulus.
In the .tran command, we add SWEEP command to change the values for the ones in OPTIMIZE; the function OPTIMIZE will search for the best values for p1, and the optimization results will be equal to the difference between trigger rising propagation delay and trigger falling propagation delay with the aim of reaching zero.
Below that, we measure tpdr, tpdf and even calculate the average propagation delay.

## Slide 22: P/N Results
P/N ratio for equal delay is 2.9:1
  tpd = tpdr = tpdf = 17.9 ps (slower than 2:1 ratio)
  Big pMOS transistors waste power too
  Seldom design for exactly equal delays
What ratio gives lowest average delay?
  .tran 1ps 1000ps SWEEP OPTIMIZE=optrange RESULTS=tpd MODEL=optmod
  P/N ratio of 1.8:1
  tpdr = 18.8 ps, tpdf = 15.2 ps, tpd = 17.0 ps
P/N ratios of 1.5:1 – 2.2:1 gives tpd < 17.2 ps
Notes: The results of running this code will output that of P/N ratio, which shows that for equal delay, a ratio of 2.9 to 1 will be necessary.
Given a time of tpd, tpdr, and tpf of 17.9 picosecond, which is slower to our default ratio.
Big pmos transistor wastes power too; this is a seldom design for exactly equal delays.
But lower average delay, the P/N ratio should be 1.8 to 1.
P/N ratios of 1.5 to 1 and 2.2 to 1 give tpd of less than 17.2 pico seconds.

## Slide 23: Power Measurement
HSPICE can measure power
  Instantaneous P(t)
  Or average P over some interval
  .print P(vdd)
  .measure pwr AVG P(vdd) FROM=0ns TO=10ns
Power in single gate
  Connect to separate VDD supply
  Be careful about input power
Notes: HSPICE can measure instantaneous power P(t) or average P over some interval.
You will need to add the command .print P(vdd) or .measure pwr AVG P(vdd) and the period by entering the From and to values.
If you want to calculate the power in a single gate, connect it to a separate Vdd supply, but be careful about the input power.

## Slide 24: Logical Effort
Logical effort can be measured from simulation
  As with FO4 inverter, shape input, load output
Notes: Another thing that can be measured through the SPICE simulation is the logical effort.

## Slide 25: Logical Effort Plots
Plot tpd vs. h
  Normalize by τ
  y-intercept is the parasitic delay
  Slope is logical effort
Delay fits straight line
very well in any process
as long as input slope is
consistent
Notes: To do it, you can plot the propagation delay against H and normalize by τ(Tau). Where y-intercept is the parasitic delay and the slope is the logical effort.
The delay fits a straight line very well in any process as long as input is consistent.

## Slide 26: Logical Effort Data
For NAND gates in IBM 65 nm process:
Notes:
  Parasitic delay is greater for outer input
  Average logical effort is better than estimated
Notes: In some cases, there is available data for the logical effort of some components, for example:
For NAND gates in IBM 65 nm process.

## Slide 27: Comparison