## Slide 1: CMOS VLSI Design Lecture 15: Datapath Functional Units
Notes: Hello and welcome.

## Slide 2: Learning Objectives
At the end of this lecture, you should be able to
Design and describe the operation of datapath circuits such as comparators, shifters, multi-input adders and multipliers.

## Slide 3: Comparators
0’s detector: A = 00…000
1’s detector: A = 11…111
Equality comparator: A = B
Magnitude comparator: A < B
Notes: Comparators are used to detect patterns in binary numbers.
A 0’s/1’s detector will indicate when all the bits are 0’s/1’s, respectively.
An equality comparator compares two binary operators.

## Slide 4: 1’s & 0’s Detectors
1’s detector: N-input AND gate
0’s detector: NOTs + 1’s detector (N-input NOR)
Notes: Circuit shows 1’s detector using N-input AND gates.
It is shown that a )’s detector can be realized from a 1’s detector by negating all its inputs.

## Slide 5: Equality Comparator
Check if each bit is equal (XNOR, aka equality gate)
1’s detect on bitwise equality
Notes: Equality detector between two binary numbers of each N-bits can be realized using N XNOR gates plus an N-input AND gate.

## Slide 6: Magnitude Comparator
Compute B – A and look at sign
B – A = B + ~A + 1
For unsigned numbers, carry out is sign bit
Notes: Circuit shows a magnitude comparator. It basically subtracts A from B. The circuits at the output determines if A is less than, greater than or equal to B.

## Slide 7: Signed vs. Unsigned
For signed numbers, comparison is harder
  C: carry out
  Z: zero (all bits of A – B are 0)
  N: negative (MSB of result)
  V: overflow (inputs had different signs, output sign ≠ B)
  S: N xor V (sign of result)

## Slide 8: Shifters
Logical Shift:
  Shifts number left or right and fills with 0’s
    1011 LSR 1 = 0101 1011 LSL1 = 0110
Arithmetic Shift:
  Shifts number left or right. Rt shift sign extends
    1011 ASR1 = 1101 1011 ASL1 = 0110
Rotate:
  Shifts number left or right and fills with lost bits
    1011 ROR1 = 1101 1011 ROL1 = 0111
Notes: Three types of shifts mentioned here.
Note tail
Logical shift, an operation in which the binary number is shifted either left or right with a 0 added at the tail.
Arithmetic shift, an operation in which the binary number is shifted either left or right with the sign bit added at the left tail when shifted right and a zero added to the right tail when shifted left.
Rotate an operation in which the binary number is shifted right or left with tail replaced with the previous bit at the head.

## Slide 9: Funnel Shifter
A funnel shifter can do all six types of shifts
Selects N-bit field Y from 2N–1-bit input
  Shift by k bits (0 ≤ k < N)
  Logically involves N N:1 multiplexers
Notes: A funnel shifter can perform all six types of shift operations (Logical Shift Right & Left; Arithmetic Shift Right & Left; and Rotate Right & Left).

## Slide 10: Funnel Source Generator

## Slide 11: Array Funnel Shifter
N N-input multiplexers
  Use 1-of-N hot select signals for shift amount
  nMOS pass transistor design (Vt drops!)
Notes: An array funnel shifter can be designed using a nMOS pass transistors, although this circuit suffers from Vt drops.

## Slide 12: Logarithmic Funnel Shifter
Log N stages of 2-input muxes
  No select decoding needed

## Slide 13: 32-bit Logarithmic Funnel
Wider multiplexers reduce delay and power
Operands >32 bits introduce datapath irregularity

## Slide 14: Barrel Shifter
Barrel shifters perform right rotations using wraparound wires.
Left rotations are right rotations by N – k = k + 1 bits.
Shifts are rotations with the end bits masked off.
Notes: A barrel shifter is a digital circuit that can shift a data word of N-bits to up to N-1 places in right or left direction.

## Slide 15: Logarithmic Barrel Shifter
Notes: Logarithmic barrel shifter can be built using a combination of multiplexers and a sign mask. The logarithmic barrel shifter can perform arithmetic shifts, which is a signed shift and logical shift in both left and right directions.

## Slide 16: 32-bit Logarithmic Barrel
Datapath never wider than 32 bits
First stage preshifts by 1 to handle left shifts

## Slide 17: Multi-input Adders
Suppose we want to add k N-bit words
  E.g., 0001 + 0111 + 1101 + 0010 = 10111
Straightforward solution: k-1 N-input CPAs
  Large and slow
Notes: This carry-propagate adder structure is large and can grow with K.

## Slide 18: Carry-Save Addition
A full adder sums 3 inputs and produces 2 outputs
  Carry output has twice the weight of sum output
N full adders in parallel are called carry-save adder
  Produce N sums and N carry outs
Notes: A carry-save adder efficiently computes the sum of three or more binary numbers and produces a sum and carry output.

## Slide 19: CSA Application
Use k-2 stages of CSAs
  Keep result in carry-save redundant form
Final CPA computes actual result
Notes: To get the result of the addition of K N-bit numbers, the outputs (carry outputs ) using a carry-save adder, one would need K-2 CSA stages plus a CPA adder.

## Slide 20: Multiplication
Example:
M x N-bit multiplication
  Produce N M-bit partial products
  Sum these to produce M+N-bit product
Notes: Multiplication steps involve partial products and sum of the partial product.

## Slide 21: General Form
Multiplicand: Y = (yM-1, yM-2, …, y1, y0)
Multiplier: X = (xN-1, xN-2, …, x1, x0)
Product:
Notes: This slide breaks down the steps for the multiplication of two binary numbers.

## Slide 22: Dot Diagram
Each dot represents a bit
Notes: Dot diagram to illustrate partial product. Each dot represents the product of two bits

## Slide 23: Array Multiplier
Notes: An array multiplier has a regular structure of digital combinational circuit that will multiply two binary numbers using an array of adders.

## Slide 24: Rectangular Array
Squash array to fit rectangular floorplan

## Slide 25: Fewer Partial Products
Array multiplier requires N partial products
If we looked at groups of r bits, we could form N/r partial products.
  Faster and smaller?
  Called radix-2r encoding
E.g., r = 2: look at pairs of bits
  Form partial products of 0, Y, 2Y, 3Y
  First three are easy, but 3Y requires adder 

## Slide 26: Booth Encoding
Instead of 3Y, try –Y, then increment the next partial product to add 4Y
Similarly, for 2Y, try –2Y + 4Y in the next partial product
Inputs |  |  | Partial Product | Booth Selects |  | 
X2i+1 | X2i | X2i-1 | PPi | SINGLEi | DOUBLEi | NEGi
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | Y | 1 | 0 | 0
0 | 1 | 0 | Y | 1 | 0 | 0
0 | 1 | 1 | 2Y | 0 | 1 | 0
1 | 0 | 0 | -2Y | 0 | 1 | 1
1 | 0 | 1 | -Y | 1 | 0 | 1
1 | 1 | 0 | -Y | 1 | 0 | 1
1 | 1 | 1 | -0(=0) | 1 | 0 | 1
Notes: Booth encoding is a method used to reduce the number of partial products in the multiplier.

## Slide 27: Booth Hardware
Booth encoder generates control lines for each PP
  Booth selectors choose PP bits

## Slide 28: Sign Extension
Partial products can be negative
  Require sign extension, which is cumbersome
  High fanout on most significant bit

## Slide 29: Simplified Sign Ext.
Sign bits are either all 0’s or all 1’s
  Note that all 0’s are all 1’s + 1 in proper column
  Use this to reduce loading on MSB

## Slide 30: Even Simpler Sign Ext.
No need to add all the 1’s in hardware
  Precompute the answer!

## Slide 31: Advanced Multiplication
Signed vs. unsigned inputs
Higher radix Booth encoding
Array vs. tree CSA networks